## Slide 1: Measurement of the Charge and Light Yield of Low Energy Electronic Recoils in Liquid Xenon at Different Electric Fields
Matthew D. Anthony
April 12, 2015
Notes: Hi, my name is Matt Anthony and I will be presenting on the upcoming results of an experiment performed at Columbia University’s Nevis Labs measuring the light and charge yield of electronic recoils in LXe at low energies and at different electric fields.

## Slide 2: Motivation
LXe experiments lead direct dark matter scattering search
  Xenon100, LUX, Xenon1T
Dual-phase detectors  simultaneously detect light and charge
  Prompt light emission from interaction in LXe (S1)
  Complementary signal from acceleration of electrons through GXe (S2)
Leads to S2 if remains free
S1
S1
Notes: Dual-phase detectors
  Particle interacts and excites and ionizes – different amount depending on type of particle
  Excitation + recombination lead to prompt scintillation, S1
  Free electrons drifted to gas layer lead to proportional scintillation, S2
Currently, LXe experiments lead the search in many types of dark matter interactions. As many of you likely know, these types of detectors are called dual-phase since they contain both LXe and GXe. The concept of these detectors is fairly straight-forward: a particle comes into the LXe portion of the detector and interacts. This interaction will excite and ionize xenon atoms (in different amounts depending on the type of particle – useful for discrimination). The excitation of xenon atoms and the ionization + recombination lead to prompt light emission, known as the S1 signal, and the free electrons, when drifted to the gas layer and accelerated through, produce the proportional scintillation signal, known as the S2 signal.

## Slide 3: Motivation
Goal: improve understanding of low energy interactions in LXe
  Given an electronic or nuclear recoil at a certain energy in a drift field, how much light and charge do you expect to be produced?
  Light and charge yield non-linear in energy and drift field
    Light Yield = Photoelectrons / Energy
    Charge Yield = Free Electrons / Energy
Leads to S2 if remains free
S1
S1
Notes: Improve understanding of interactions in LXe by characterizing light and charge yield at lw energies and different fields
  Explain light and charge yield
Plot on left
  Charge and light, relative to zero field, as a function of different fields for different particles
  Notice anti-correlation in light and charge - influenced by field dependence of recombination
    High fields you lower recombination probability and increase number of free electrons and hence S2 while reducing S1
The main goal of our study is to improve our understanding of interactions in LXe by characterizing the light and charge yield at the lowest energies and at different fields. By light yield I will be referring to the number of photoelectrons detected for a given interaction energy and by charge yield I will be referring to the number of free electrons produced for a given interaction energy. In the plot on the left, we have the charge and light seen (relative to zero field) as a function of drift field. As you can see, the amount of light and charge seen are very dependent on the field and the type of particle interacting. This is mainly influenced by the recombination step seen in the energy diagram on the right. At higher fields you lower the recombination probability and increase the number of free electrons drifting to the GXe, which in turn increases the S2 while reducing the S1.

## Slide 4: neriX Detector
Dual-phase LXe Time Projection Chamber for measuring nuclear and electronic recoils in Xenon
  Small size and minimal materials surrounding fiducial volume make this detector well-suited for measurements of the light and charge yield
  Unlike most previous measurements, can measure the light yield as a function of drift field applied
  Pursue light and charge yields as low as 1 keV
Notes: Large detectors ideal for DM detection, but strengths are weakness for measuring low energy yields
Constructed “shrunken-down” version called neriX
  Much smaller in size (2 kg) and does not have shielding or extra materials around TPC
  Dual-phase => measure light and charge yield simultaneously
neriX is almost unique – can measure light yield as a function of energy and drift field
  Extremely important given that larger detectors are operated with an applied electric field and given the quenching of S1 discussed earleir
While large detectors are ideal for dark matter detection, their strengths quickly become weaknesses for measuring low energy yields. For this reason, a special “shrunken-down” version of the famous dark matter detectors was built called neriX. neriX is much smaller in size, holding only roughly 2 kg of Xe, and does not have the shielding and extra materials that its larger cousins have. neriX is also a dual-phase detector so it is able to simultaneously measure the light and charge yield. Unlike most previous measurements, neriX is able to measure the light yield both as a function of energy and drift field, which is extremely important since dual-phase detectors are operated with an applied electric field and given the quenching of S1 discussed earlier.

## Slide 5: neriX Detector
Very similar design to its much larger cousins
  Dual-phase (S1 and S2)
  3D Position Reconstruction
  Stable cryogenics system
PMTs
  4 1’’ square 4 channel PMTs on top (total of 16 channels)
  1 2’’ diameter HQE PMT on bottom
Component | Voltage [kV]
Anode Grid | 4.5
Gate Grid | 0
Shaping Rings | 0
Cathode Grid | -0.345, -1.054, -2.356, -5.500
Bottom Mesh | 0
Notes: As mentioned before, dual-phase
  Hand-in-hand with dual phase is 3D position reconstruction
On the right is a schematic of the detector
  Bottom: 2’’ diameter HQE PMT, used for yield analyses
  Top: 4 1’’ square four anode PMTs – all intents and purposes are 16 separate PMTs
As mentioned before, the detector is dual-phase and coming hand-in-hand with this is the ability to reconstruct the location of an interaction in the detector in three dimensions. On the right is a schematic of the detector. At the bottom of the TPC, we have a single 2’’ diameter HQE PMT, used for the yield analyses, and at the top of the TPC we have four 1’’ square four anode PMTs. These four PMTs are, for all intents and purposes, 16 separate PMTs which are used mainly for position reconstruction.

## Slide 6: Drift Fields
Measured the light and charge yield at four different drift fields
  All components but cathode kept constant between setups
  Simulations of the field performed in Comsol
Component | Voltage [kV]
Anode Grid | 4.5
Gate Grid | 0
Shaping Rings | 0
Cathode Grid | -0.345, -1.054, -2.356, -5.500
Bottom Grid | 0
Cathode Voltage [kV] | Drift Field [V/cm]
-0.345 | 210
-1.054 | 490
-2.356 | 1000
-5.500 | 2250
Notes: Design of TPC very similar to other dual-phase Lxe experiments
  Liquid level between gate and anode – electron extraction for S2
  Cathode kept at negative HV to produce different electric fields
    Cathode values used and corresponding fields in the table on the left
    For reference, Xenon100 operates at drift field 500 V/cm and Xenon1T plans on using 1kV/cm
The actual design of the TPC is very similar to that of other dual-phase LXe experiments. The liquid level extends from the bottom PMT to just above the gate grid. The anode is kept at 4.5 kV and the gate grid at ground to produce a large electric field to extract and accelerate the electrons through the gas. The cathode grid is kept at negative high voltage and produces a drift field between itself and the gate grid. To produce the different electric fields, we only change the negative HV on the cathode. The cathode values used and corresponding drift fields are in the table on the left. For reference, Xenon100 uses a drift field of approximately 500 V/cm and Xenon1T plans on using a 1 kV/cm field.

## Slide 7: Single Photoelectron and Electron Detection
Single Photoelectron Gain
  Use LED at low light level to measure SPE gain
  Relatively low gain (~4-7 x 105 e-) to avoid saturation
  Use background subtraction and coincidence cut to clean distribution
Single Electron Gain
  Use photoionization of cathode by S2 to find small numbers of electrons
SPE Gain Calibration
Single Electron Gain
More details on single electron gain: J. Phys. G: Nucl. Part. Phys. 41 (2014) 035201
Photoionization of Gate and Cathode
Notes: Prerequisite for yield measurement is ability to detect single photoelectrons and electrons
neriX PMTs at relatively low gain (4-7*10^5 e-) so additional steps required to determine SPE gain
  The final product of the SPE gain determination is located in the top right figure in blue
Able to determine gain of single electrons
  Large S2 events produce enough light to free electrons from the gate and cathode grid
  These electrons are drifted through the TPC and create additional S2 signals after the main S2
    In the bottom center plot, you can see the peaks in time after the main S2
One necessary feature of the detector is the ability to detect single photoelectrons and electrons. neriX PMTs operate at relatively low gains compared to most experiments (4-7 x 10^5) which requires additional steps in the calibration. To start, a background measurement is made, followed by a measurement at a very low LED light level such that no photons are seen most of the time. We then make a coincidence cut to remove a large portion of null events in both samples (grey in the histogram being with the LED and purple in the histogram being the background) and then finally background subtract resulting in the blue specturm. The mean of the resulting distribution is taken to be the value of the gain.
We are also able to determine the gain of a single electron. After large S2 events, some of the emitted photons will actually release electrons from the cathode and gate mesh. These electrons will then travel via the drift field back to the liquid gas boundary where they are accelerated through. We therefore make a time cut after our main S2 signal to find these single electron events. This process can also be used to calculate the drift velocity of the electrons through xenon by comparing the time it takes to produce the S2 for electrons freed from the gate (red peak in the bottom left histogram) and the cathode (blue peak in the histogram).
Also use the photoionization to measure the drift velocity at given fields

## Slide 8: Position Reconstruction
Similar to larger LXe detectors, neriX is able to reconstruct the 3D position of an event
  More difficult given small size of the detector
  Used Geant4 construction of the detector to simulate S2 patterns at given positions
  Train neural network on the simulation using FANN open source library
  Average error of simulated data inside radius of 18 mm ≅ 0.5 mm
FANN
Co-57 Position Reconstruction
Simulated vs. Reconstructed Position
Notes: neriX is able to reconstruct position in three dimensions
Use FANN open source library to train neural network on simulated S2 events
FANN acts like a black box during processing – takes in normalized amount of proportional light seen by each PMT and outputs an XY position
Center plot is a test of the FANN reconstruction
  X-axis is the simulated radius and y-axis is reconstructed radius
  Very good agreement up to 18 mm and in fact an average error of 0.5 mm
  Radius of detector is 21 mm
On the right is an actual XY map for a Co-57 calibration
  Can actually see the pattern of the gate mesh since the field is slightly stronger at those locations
neriX is able to reconstruct the position of an event in three dimensions. To do this we use the FANN open source library to train a neural network on simulated S2 events. The FANN then acts as a black box during processing, taking in the normalized amount of proportional light seen by each PMT and outputting an XY position. In the center plot, we have a test of the NN reconstruction. On the x-axis is the simulated radius and on the y-axis is the reconstructed value of the radius. As you can see, we have very good agreement up to 18 mm, the radius of the detector being 21 mm, and actually achieved an average error of 0.5 mm up to this radius.
On the right is the position reconstruction for a Co-57 calibration, in which you can actually see the gate grid pattern in the XY map since the extraction field is strongest at those points.

## Slide 9: Compton Coincidence Technique
Energy deposited in LXe determined using Compton Coincidence Technique
  Photons Compton scatter in LXe then deposit remaining energy in HPGe detector
Notes: Heard me repeat how neriX’s small size is ideal for this type of measurement – hopefully after this slide it will be clear why!
To determine light yield, we must know S1, S2, the field, and the energy
  Already discussed how to find the first three, so all that remains is determining the energy
  Will do this via the Compton coincidence technique
Place Cs-137 source on one side of detector and HPGe on the other
  HPGe has extremely good resolution around 662 keV line
Idea is that photons will leave the source, interact once in the xenon via a Compton scatter, creating an S1 and an S2, and then be fully absorbed in the Ge
  Thus, to find energy just subtract energy deposited in Ge from starting photon energy
Use coincidence trigger between Lxe, specifically the S2, and Ge to cut on good events
Why is neriX’s small size so important?
  Reduced double scatters since less liquid xenon
  Reduced accidental scatters with external materials given minimalistic design
You have heard me say several times how neriX’s small size is ideal for this type of measurement – hopefully the reason for this will be clear after this slide! To determine the light and the charge yield, we are using the Compton coincidence technique. How we determine the S1, the S2, and the field has already been covered – all that remains is how we determine the energy of the interaction.
To do this, we place a Cs-137 source on one side of the detector and a HPGe detector on the other side. The HPGe detector is used because it has extremely good energy resolution around the 662 keV line. The idea is that photons emitted from the source will interact in the LXe via a Compton scatter, creating an S1 and S2, and then be fully absorbed in the HPGe. To cut on good events, we use a coincidence trigger between the LXe, specifically the S2, and HPGe signal. To find the energy of these good events, you simply subtract the energy deposited in the HPGe from the known starting energy, which in our case was 662 keV.
Because the detector is small and compact, we minimize the chance of double scatters in the detector and because of the minimalistic design outside of the TPC, we reduce the chance of accidental scatters outside of the LXe.

## Slide 10: Coincidence Spectrum
Preliminary
Below are two sample coincidence spectra that are used to determine the light and charge yield at a given energy
Prompt Scintillation Light (S1) vs. Energy Deposited in LXe
Proportional Scintillation Light (S2) vs. Energy Deposited in LXe
All data are preliminary
Preliminary
Preliminary
Notes: Before continuing, I would like to note that ALL DATA ARE PRELIMINARY
Shown here are our two coincidence spectra at a single drift field
On the y-axis of each is the energy deposited in the Ge subtracted from the starting energy of the photon
X-axis on the left plot is S1 and x-axis on right plot is S2 signal
We project this spectra into S1 and S2 space after making energy cuts and the resulting plot can be seen below each spectrum
Finally, to determine the yield, we fit these final spectra with a Gaussian
  This procedure continued down to 1 keV
The two top figures on this slide are sample coincidence spectra. On the y-axis of each is the energy deposited in the LXe (determined by subtracting the energy deposited in HPGe from the initial energy of the photon) while the x-axis on the left plot is the S1 signal and x-axis on the right plot is the S2 signal.
Below these are the projections of the above plots into S1 and S2 space, respectively AFTER a cut in the energy. To determine the light and the charge yield at a certain energy and drift field, you simply fit these spectra.

## Slide 11: Electronic Recoils: Light and Charge Yields
By projecting energy slices in the previous plots into S1 and S2, we can fit the remaining spectrum for the yield
Above are preliminary results for the light and charge yield at different drift fields
Light Yield vs. Recoil Energy
Charge Yield vs. Recoil Energy
Notes: By looking at each energy slice at each field, you produce the following light and charge yield plots
  Again, THESE RESULTS ARE PRELIMINARY AND SUBJECT TO CHANGE
On the x-axis for each plot is the recoil energy and on the y-axis of the left plot is the light yield and on the y-axis of the right plot is the charge yield
The different color marks represent the different drift fields used
While these plots only go down to 3 keV, we did measure down to 1 keV
We are still working on finalizing our low energy analysis and our absolute yield determination
By looking at each energy slice at each field you can produce the following yield plots and these are the preliminary results for our measurement of the light and charge yield of LXe. On the y-axis is light yield for the left plot and the absolute charge yield for the right plot. The absolute yield means that we have accounted for extraction efficiency. On the x-axis for both plots is the energy of the interaction in the xenon. The different color marks represent the different drift fields used. Please note that while these plots only go as low as 3 keV, we did measure down to 1 keV.
Still working on absolute light yield – must account for light collection efficiency which is an ongoing analysis.

## Slide 12: Electronic Recoils: Light and Charge Yields
S1 and S2 anti-correlated with respect to field
Below 10 keV, light yield increases with energy and charge yield decreases with energy for all fields
Light and charge yield measured down to 1 keV – stay tuned!
Light Yield vs. Recoil Energy
Charge Yield vs. Recoil Energy
Notes: A few important trends to notice
  S1 and S2 anti-correlated with respect to field – as you increase the drift in Lxe, the S1 signal is reduced but the charge yield increases
    Good agreement with the previous results mentioned earlier at a single energy
  Below 10 keV, light yield increases with energy while charge yield decreases with energy
Again, we are still working on finalizing our low energy analysis and our absolute yield determination so please stay tuned for the final results!
A few important trends to notice with these plots.
First, the S1 and S2 are anti-correlated with respect to field. As you increase the drift field in the LXe, the S1 signal is reduced but the charge yield increases. This is in good agreement with the previous results mentioned earlier at a single energy.
Second, below 10 keV, light yield increases with energy while charge yield decreases with energy.
Again, we measured the light and charge yield down to 1 keV and are completing absolute yield analyses so please stay tuned for the final results!

## Slide 13: Nuclear Recoils: Light and Charge Yields
In coming months, will perform very similar measurement with neutron source
Similar concept but with additional complications
  No energy resolution in liquid scintillators – completely dependent on scattering angle for determination of energy deposited in LXe
  Must account for neutron time of flight in coincidence trigger
Notes: I wanted to take a little time to mention our upcoming measurement of the light and charge yield for nuclear recoils
  We are in the process of preparing neriX for this run and hopefully will begin soon
  Measurement will be similar to electronic recoil measurement but with Cs source replaced by a neutron generator and the Ge replaced by multiple liquid scintillators
Thank you for your time.
I wanted to take a little time to speak about our upcoming measurement of the light and charge yield for nuclear recoils. We are in the process of preparing neriX for its second run and hopefully will begin shortly.
This measurement will be very similar to the electronic recoil measurement with the Cs source replaced by a neutron generator and the HPGe replaced by multiple liquid scintillators.
While similar, this experiment will have a few added complications. For example, the liquid scintillator we use has no energy resolution, only pulse shape discrimination, so energy is completely determined by the scattering angle inside the LXe. Also, the neutron time of flight is much more difficult to account for in the coincidence trigger compared to the photon time of flight. Ultimately though, we hope to measure the light and charge yield for nuclear recoils down to 1 keV as well.